September 28, 2020

Notice of Addendum to: RFP; NCSO-20-R-001: NASSAU COUNTY SHERIFF’S OFFICE PUBLIC SAFETY TRAINING COMPLEX

ADDENDUM NCSO-20-R-001-2

Notice is hereby given regarding the Nassau County Sheriff’s Office (“NCSO”) solicitation for Request for Proposal (“RFP”) for SAND, (fill material) – Nassau County Sheriff’s Office Public Safety Training Complex.  The following revisions are being made to the original Request for Proposal.

Revision to Section:

III.

A. Deliverables Description:

The product is Sand (fill material) to be delivered to the Nassau County Sheriff’s Office Public Safety Complex located off highway 108 in north central Nassau County. All bids will be based on a “per cubic yard price” delivered to the site. All charges related in any way will be included in the “per cubic yard pricing”. No additional delivery fees or add on charges will be accepted. The estimated Sand (fill material) is approximately seventy one thousand two hundred and fifteen (71,215) cubic yards.

The fill for the earthwork at the NCSO Gun Range shall be predominately sand.  Sand gradation is defined as being between the US Standard No. 4 sieve and the No. 200 sieve.  The sand fill may have up to 5 percent of the fill larger than the No. 4 Sieve (gravel and woody material), but no particles can be larger than 0.5 inch and no more than 20 percent of silt and clay passing the No. 200 Sieve.